How To Use Risk Evaluation To Develop A Proficiency Testing Participation Plan

Speaker: Jia-Fen Cheng

Taiwan Accreditation Foundation

188 Gong-Dao 5 Road, Sec. 3, Hsinchu, Taiwan

Tel: +886-3-5714848   Fax: +886-3-5726308   e-mail: cherry@taftw.org.tw

Authors: Pao-Chu Kao, Shu-Fen Chang, Ju-Lin Wei , and Jia-Chi Chen

Taiwan Accreditation Foundation

Abstract

In the past, the proficiency testing items and participation frequency were formulated by accreditation bodies, regardless of the scale, customer type, and economic conditions of a laboratory. In 2010, ILAC P9 require the applicant laboratories considering needs and risk level to make their own proficiency testing participation plan , as long as proficiency testing program feasible both logistically and economically. In response to the requirements of ILAC P9, Taiwan Accreditation Foundation (TAF) revised the accreditation criteria document-- Requirements for proficiency testing activities. Submit a PT plan prepared by the laboratory seeking for accreditation is required in this revised document. To facilitate applicants to learn how to make a plan and implement thereafter, a guideline was developed by TAF based on the concept of risk evaluation. This paper will describe how to use qualitative risk analysis methodology to analyze the risk level of the factors affecting correctness/reliability of measurement results. The determining factors include experience, competence and turnover rate of staff, traceability sources, stability of measurement technique, number of tests, and significance and final use of the testing data, as mentioned in EA-4/18.

Learning Objectives

The readers (listeners) will learn how to develop and revise their proficiency testing participation plan by evaluating risk level of some important factors, which affect the correctness/reliability of measurement results.

1.	Introduction

The ILAC P9 ratified in 2010 presents a new concept for traditional methods – the accreditation organization shall establish a uniform set of levels and frequencies for the proficiency testing activity participation of laboratories; that is, the laboratory shall consider its own requirements and levels of risk and formulate its own Proficiency Testing Participation Plan (hereafter referred as the PT plan for short). The accreditation organization should not only define the minimum requirements for proficiency testing participation (levels and frequency), but also review whether the PT plan of the laboratory is consistent with the scope of accreditation and provide the necessary guidance.

In the TAF Requirements for Proficiency Testing Activity (TAF-CNLA-R05)[1], it is specified that the laboratory applying for calibration/testing/medical activities should present the respective PT plans for the activities under application and/or for accreditation based on the routine quality control/assurance measures and acceptable levels of risks of the laboratory.  The laboratory shall regularly review its plan and amend specifics of the plan to meet existing conditions.  The TAF staff of the chemical testing field, when compiling domestic and international related information, did not find any existing reference literature providing information on the means by which a PT plan may be formulated from risk assessment concepts; for instance, the EA-4/18 document(Guidance on the level and frequency of proficiency testing participation)[2] merely defines the principles of estimation, determining factors, and several case study for examples and discuss the types of sub-disciplines from a technical perspective without providing a complete PT plan example. In order to allow the laboratory to quickly learn the procedure in formulating its PT plan and undertake to realize the plan, the TAF shall, under the spirit of the EA-4/18, classify the extent of the threat imposed by factors affecting the accuracy/reliability of the testing results to assist in assessing the levels of risks based on the frequency of their occurrences. Four difference chemical laboratory cases were selected for case studies based on the variant complexities or simplicities of their initial accreditation, extending accreditation, renewal accreditation, and scopes of accreditation to provide laboratories with references for their respective PT plan formulation and implementation. These case studies are as provided in the TAF Guidelines for Establishing Plans of Participation in Proficiency Testing Programs (TAF-CNLA-G29).

This paper will take one particular case study to illustrate how to put the risk assessment concepts into the consideration points, formulation procedure, and subsequent review and amendment procedures of the PT plan.

2.	Key Considerations and Implementation Procedures in the Formulation of the PT Plan

Not all testing activities have available corresponding proficiency testing programs for participation; hence, in consideration of the supply and economic costs, the laboratory may classify sub-disciplines based on the measurement techniques, measurement properties, and product types. After a sub-discipline has been determined, the laboratory may formulate the minimum frequency of proficiency testing participation for each respective sub-discipline based on the level of risk involved. As for the acceptable level of risk of the laboratory, the following factors may be included for considerations:

(1)	Integrity of the quality control/assurance measures

(2)	Number of tests undertaken

(3)	Turnover of technical staff

(4)	Experience and knowledge of technical staff

(5)	Source of Traceability (e.g. availability of reference materials, national standards, etc.)

(6)	Known stability/instability of the measurement technique

(7)	Significance and final use of testing data

The laboratory may formulate its PT plan according to the following procedure.

3.	Case Study of PT Plan

In general, a laboratory possessing the required technical competence would undertake to classify sub-disciplines and encounter no serious problems in the process; the difficulty lies in the acquiring a balance between supply and cost considerations and in reducing risks down to a minimum. Risk assessment is defined as a quantification of the various consequential effects and losses of a particular risk event after its occurrence. The assessment procedure shall cover the following aspects:

a.	Risk features: probability of occurrence, duration of the risk, and key risk points ;

b.	Mode of action: direct or indirect effects (range)

c.	Consequences of risk occurrence: losses and benefits

The more commonly used risk assessment methods include the following: knowledge-based analysis method, model-based analysis method, qualitative analysis, and quantitative analysis. The case study presented in the following employ the qualitative risk analysis methods, and different ratings are given based on the existing conditions of the respective factors for consideration. Thereafter, the level of risk involved is determined based on the risk matrices, and pursuant to which, the imperativeness and frequency of proficiency testing participation are determined.

In the following, a case study of a laboratory engaging in the chemical testing of metals, textiles, and food products is presented to explain the formulation process of a PT plan pursuant to the foregoing procedure.

3.1	Prepare a list of the testing items

List should include, at least, the accredited items and items to be accredited of the laboratory. Enumerate the items to be tested(products), testing properties(or parameters), testing methods, and measurement techniques/instruments as shown in Table 1.

Table 1. List of testing items.

| Item No. | Product | Property | Method | Measurement technique/instrument |
| --- | --- | --- | --- | --- |
| 1 | Low-alloy steel | Elemental analysis | CNS 10006 ASTM E415 | Photoelectric Emission Spectrometric Analysis |
| 2 | High-alloy steel | Elemental analysis | CNS 10006 ASTM E1086 | Photoelectric Emission Spectrometric Analysis |
| 3 | Aluminum alloy | Elemental analysis | ASTM E1251 | SPARK-OES |
| 4 | Bronze casting | Composition analysis | CNS 4125 | ICP-AES |
| 5 | Brass castings | Composition analysis | CNS 4336 | ICP-AES |
| 6 | Textiles | Warp and weft density | CNS 12915 sec 6.6 | NA |
| 7 | Textiles | Air permeability | CNS 5612 | Air-permeability Tester |
| 8 | Textiles | Fiber Composition | CNS 2339 | Manual separation |
| 9 | Textiles | Colorfastness to Perspiration | CNS 1496 | Perspiration Tester |
| 10 | Textiles | Colorfastness to Washing | CNS1494 A-1、A-2、A-3、B-1、B-2、B-3、B-4、C-1、C-2、C-3、C-4、C-5 | Washing Fastness Tester |
| 11 | Textiles | Colorfastness to Rubbing | CNS 1499 Model I & II | Colorfastness to Rubbing tester |
| 12 | Textiles | Anti-ultraviolet | AS/NZS 4399 | Radiation spectrometer |
| 13 | Textiles | Water repellency | CNS 10461 | Spray test device |
| 14 | Textiles | Dryness | CNS 12915 | Drying time measuring device |
| 15 | Textiles | Mass | CNS 12915 sec 6.4 | Balance |
| 16 | Packaged Drinking Water | Heavy metal | NIEA W311.51B | ICP-AES |
| 17 | Jam | Preservative | CNS 10949 | GC-FID |
| 18 | Vegetables, fruits | Pesticide Residues | TFDA method No. 0991900925 | LC/MS/MS |
| 19 | Apple Juice | pH | CNS 6492 | pH meter |
| 20 | Apple Juice | Acidity | CNS 8626 | pH meter & Titrator |
| 21 | Apple Juice | Sugar content | CNS 12569 | Abbe Refractometer |
| 22 | Pork meat | Residue of Veterinary Drugs - tetracycline | TFDA method No. 0939300627 | LC/MS/MS |
| 23 | Aquatic products | Residue of Veterinary Drugs -Nitrofuran Metabolites | TFDA method No. 0991900821 | LC/MS/MS |
| 24 | Shrimp | Residue of Veterinary Drugs -Malachite Green and its Metabolite | TFDA method No. 0971800008 | LC/MS/MS |

3.2	Determine the sub-disciplines

Classify the sub-discipline based on the respective measurement techniques, testing properties, and differences of the products to be tested; and provide technical bases for classification.

In the aforementioned 24 test items, the measurement techniques employed for testing metals include the Photoelectric Emission Spectrometric Analysis, SPARK-OES, and Inductively Coupled Plasma with Atomic Emission Spectrometer. According to the differences and similarities of the measurement techniques, the five accredited items may be classified into 3 sub-disciplines for metal products. In light of the variances of the measurement techniques used in the 10 accredited items, no further classification may be conducted on textiles. For food products, 9 accredited items are categorized into 6 sub-disciplines in accordance to the measurement techniques. Thus, a total of 19 sub-disciplines are classified; classification results are as presented in Table 2.

Table 2. Sub-discipline classification.

| Product | Measurement technique/instrument | Property | Item No. | Sub-discipline No. |
| --- | --- | --- | --- | --- |
| Metal | Photoelectric Emission Spectrometric Analysis | element | 1、2 | 1 |
|  | SPARK-OES | element | 3 | 19 |
|  | ICP-OES | composition | 4、5 | 2 |
| Textiles | NA | Warp-Weft Density | 6 | 3 |
|  | air-permeability tester | Air permeability | 7 | 4 |
|  | Manual separation | Fiber Composition | 8 | 5 |
|  | Perspiration Tester | Colorfastness to Perspiration | 9 | 6 |
|  | Washing Fastness Tester | Colorfastness to Washing | 10 | 7 |
|  | Colorfastness to Rubbing tester | Colorfastness to Rubbing | 11 | 8 |
|  | Radiation spectrometer | Anti-ultraviolet | 12 | 9 |
|  | Spray test device | Water repellency | 13 | 10 |
|  | Drying time measuring device | Dryness | 14 | 11 |
|  | Balance | Mass | 15 | 12 |
| Food | ICP-AES | Heavy metal | 16 | 13 |
|  | GC-FID | Preservative | 17 | 14 |
|  | LC/MS/MS | Pesticide Residues | 18 | 15 |
|  | PH meter, Titrator | pH、acidity | 19、20 | 16 |
|  | Abbe Refractometer | Sugar content | 21 | 17 |
|  | LC/MS/MS | Tetracycline, Nitrofuran Metabolites, Malachite Green and its Metabolite | 22、23、24 | 18 |

3.3	Principles for setting the level of risk

The level of risk for the following six key points - integrity of the quality control/assurance measures, turnover of technical staff, experience and knowledge of technical staff, source of traceability (e.g. availability of reference materials, national standards, etc.), known stability/instability of the measurement technique , and significance and final use of testing data are respectively considered in the beginning, and then the classification of the probabilities of occurrence (that is, the frequency of testing undertaken) is defined. After determining the foregoing two types of indices, the table of risk matrices is used to determine the level of risk.

3.3.1  Ratings of determining factors

Six factors from table 3 serve as the items for consideration in determining the level of risk. A level is assigned to every item on subjective consideration of the existing conditions and records of the laboratory; levels are ranked from excellent to poor expressed in ratings from 1 to 3. Generally, when a quality control measures is complete, risk is low; and when the turnover rate of technical staff is high, it means that technique could not be accumulated and thus, the risk level is high. Moreover, risk is naturally high when the technical staff does not possess sufficient experience and knowledge; when reference materials are not easily obtained or when no accredited calibration laboratory is available, traceability will be affected. On the other hand, when the measurement results are affected by the actions of the operating staff, it means that the measurement techniques are unstable; and when the testing report is often used in litigations, it means that risk is extremely high. The respective determining factors, levels, and the corresponding data sources of the laboratory are as tabulated in Table 3.

Table 3. Ratings of determining factors.

| Determining Factor | Rating | Information Source |
| --- | --- | --- |
| I. Completeness of QA measures | Completeness from high to low：1、2、3 | Testing method, quality control measures |
| II. Turnover of technical staff | Turnover rate from high to low：3、2、1 | Personnel information |
| III. Experience and knowledge of technical staff | Experience and knowledge from high to low：1、2、3 | Personnel information |
| IV. Source of traceability | Traceability from high to low：1、2、3 | Testing method、standards and reference materials |
| V. Known stability/instability of the measurement technique | Stability from high to low:1、2、3 | Quality control chart、testing method |
| VI. Significance and final use of testing data | Significance from high to low:3、2、1 | Define uses |

3.3.2  Number of tests undertaken

The number of tests undertaken and the level of risk would not be directly proportional. If the testing technique used is complicated, and the laboratory staff did not have a chance to practice the technique; therefore, the number of undertaking the tests is low means that risk is high. However, if the testing technique is simple, and the laboratory staff is familiar with the technique and the number of testing is high, this means that there would be more reports available and the probability of risk occurrence would escalate. Here we take the latter for example; the number of the tests undertaken would be expressed in the order of 1, 2, and 3 based on the quantity of the reports produced. The level and frequency of testing are as shown in Table 4.

Table 4. Rating for number of tests.

| Number of tests | Rating | Information source |
| --- | --- | --- |
| More than 30 reports a week | 3 | The number of reports issued |
| More than 30 reports a month | 2 |  |
| More than 30 reports every three month | 1 |  |

3.3.3  Level of Risk

Based on the average rating of the determining factors and the frequency of testing, the risk matrices are used to determine the level of risk; the risks are classified in three levels – high, medium, and low. Since the cycle of accreditation is three years, based on the rated level of risk – high, medium, or low – the proficiency testing participation frequency is set from once a year to once in three years, as shown in Table 5.

Table 5. Level of risk and frequency of PT participation.

| Average rating of determining factors Rating of test frequency | 1 | 2 | 3 | Level of risk | Frequency of PT participation |
| --- | --- | --- | --- | --- | --- |
| 1 | low | low | medium | low | Once per accreditation cycle |
| 2 | low | medium | high | medium | Once every two years |
| 3 | medium | high | high | high | Once per year |

3.4	Procedure of Estimating the Level of Risk

3.4.1  Determine the level of determining factors: Based on the items tabulated on Table 3, a review is conducted on the sub-discipline data. Next, determine the level of each factor based on Table 1 and sum up the levels of the six determining factors and thereafter, obtain the respective averages (rounding off shall be applied to achieve whole numbers).

3.4.2  Determine the rating of testing frequency : Frequency of tests may be obtained based on the number of reports issued per year, and then based on Table 4, rating may be obtained.

3.4.3  Obtain the level of risk: Averages rating of the determining factors and the rating of testing frequency are introduced into Table 5 to obtain the level of risk of a particular sub-discipline.

3.5	Assessing the level of risk of a sub-discipline

3.5.1  Level of risk of a sub-discipline is assessed based on the foregoing data review; results obtained are shown in Table 6.

Table 6. Risk levels of sub-disciplines.

| Sub-discipline No. | Factor/Level | Rate of Test Frequency | Level of Risk |
| --- | --- | --- | --- |
|  | I | II | III | IV | V | VI | Average |  |  |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | low |
| 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | low |
| 3 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 1 | low |
| 4 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | medium |
| 5 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | medium |
| 6 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 3 | high |
| 7 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 1 | low |
| 8 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 3 | high |
| 9 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 2 | medium |
| 10 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 1 | low |
| 11 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 3 | high |
| 12 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | low |
| 13 | 1 | 2 | 1 | 2 | 2 | 3 | 2 | 2 | medium |
| 14 | 1 | 2 | 1 | 2 | 2 | 3 | 2 | 1 | low |
| 15 | 1 | 2 | 1 | 2 | 2 | 3 | 2 | 1 | low |
| 16 | 1 | 2 | 1 | 2 | 2 | 3 | 2 | 3 | high |
| 17 | 1 | 2 | 1 | 2 | 2 | 3 | 2 | 3 | high |
| 18 | 1 | 2 | 1 | 2 | 2 | 3 | 2 | 3 | high |
| 19 | 1 | 2 | 1 | 2 | 2 | 3 | 2 | 2 | medium |

Note: The level of the determining factors is based on the status quo and subjective determination of a laboratory; hence different laboratories may produce varying assessment results.

3.5.2  According to the risk evaluation results, the participation frequency for sub-discipline are summarized in Table 7.

Table 7. Participation frequency for sub-disciplines.

| PT participating frequency | Sub-discipline No. |
| --- | --- |
| Once per accreditation cycle | 1、2、3、7、10、12、14、15 |
| Once every two years | 4、5、9、13、19 |
| Once a year | 6、8、11、16、17、18 |

Since TAF has specified the minimum requirements for designated items and the frequency of participation in the Requirements for Proficiency Testing Activity (TAF-CNLA-R05), the frequency of participation is modified accordingly. If the frequency determined based on risk assessment is higher than the requirements in TAF-CNLA-R05, the determined frequency shall be observed; however, if the frequency is lower than the requirement, frequency should be modified. Pertaining results are as shown in Table 8 (Modified items are underlined) and TAF requirements are shown in Table 9.

Table 8. Modified Participation frequency for sub-disciplines based on TAF requirement.

| PT participating frequency | Sub-discipline group |
| --- | --- |
| Once per accreditation cycle | 1、2、3、7、10、12 |
| Once every two years | 4、5、9、14、19 |
| Once a year | 6、8、11、16、17、13、15、18 |

Table 9. Participation frequency requirements for sub-disciplines in TAF-CNLA-R05.

| Product | Property | Sub-discipline No. | Designated item | Participation Frequency |
| --- | --- | --- | --- | --- |
| Metal | Elemental analysis | 1 | Yes | Once every three years |
|  | Composition | 2 | No | NA |
|  | Elemental analysis | 19 | Yes | Once every three years |
| Textile | Warp-weft Density | 3 | No | NA |
|  | Air-permeability | 4 | No | NA |
|  | Fiber composition | 5 | Yes | Once every three years |
|  | Colorfastness to Perspiration | 6 | Yes | Once every three years |
|  | Colorfastness to Washing | 7 | Yes | Once every three years |
|  | Colorfastness to Rubbing | 8 | Yes | Once every three years |
|  | Anti-ultraviolet | 9 | No | NA |
|  | Water repellency | 10 | Yes | Once every three years |
|  | Dryness | 11 | No | NA |
|  | Mass | 12 | No | NA |
| Food | Heavy metal | 13 | Yes | Once per year |
|  | Preservative | 14 | Yes | Once every two years |
|  | Pesticide Residues | 15 | Yes | Once per year |
|  | pH、acidity | 16 | No | NA |
|  | Sugar content | 17 | No | NA |
|  | Tetracycline, Nitrofuran Metabolites, Malachite Green and its Metabolite | 18 | Yes | Once per year |

3.6	Defining the Schedule of the PT Plan

The accreditation period of the laboratory is from 2012/1/2 to 2015/1/1. The PT plan of the laboratory shall be formulated within this accreditation period. Moreover, a search for proficiency testing providers shall be conducted pursuant to the TAF-CNLA-R05 information and website data. In accordance with the assessment of the risk level and the TAF-CNLA-R05 requirement, the proficiency testing participation time schedules and proficiency testing providers for the next three years are as shown in Table 10.

Table 10. Proficiency testing participation schedules.

| Sub- discipline No. | Item No | Product | Property | Method | Measurement technique /instrument | Participating frequency | Schedule | PT provider |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | Low-alloy steel | Elemental analysis | CNS 10006 ASTM E415 | Photoelectric Emission Spectrometric Analysis | Once every three years | 2012 | Proficiency Testing, Australia |
| 1 | 2 | High-alloy steel | Elemental analysis | CNS 10006 ASTM E1086 | Photoelectric Emission Spectrometric Analysis | Once every three years | 2013 | Proficiency Testing, Australia |
| 2 | 4 | Bronze casting | Composition analysis | CNS 4125 | ICP-AES | Once every three years | 2012 | CTS |
| 2 | 5 | Brass castings | Composition analysis | CNS 4336 | ICP-AES | Once every three years | 2013 | CTS |
| 3 | 6 | Textiles | density | CNS 12915 sec 6.6 | NA | Once every three years | 2014 | ASTM、TESTEX |
| 4 | 7 | Textiles | Air permeability | CNS 5612 | air-permeability tester | Once every two years | 2012 2014 | ASTM |
| 5 | 8 | Textiles | Fiber Composition | CNS 2339 | Manual Separation | Once every two years | 2012 2014 | TESTEX |
| 6 | 9 | Textiles | Colorfastness to Perspiration | CNS 1496 | Perspiration Tester | Once per year | 2012 2013 2014 | TESTEX |
| 7 | 10 | Textiles | Colorfastness to Washing | CNS1494 A-1、A-2、A-3、B-1、B-2、B-3、B-4、C-1、C-2、C-3、C-4、C-5 | Washing Fastness Tester | Once every three years | 2013 | TESTEX |
| 8 | 11 | Textiles | Colorfastness to Rubbing | CNS 1499 Model I & II | Colorfastness to Rubbing tester | Once per year | 2012 2013 2014 | TESTEX |
| 9 | 12 | Textiles | Anti-ultraviolet | AS/NZS 4399 | Radiation spectrometer | Once every two years | 2012 2014 | Not designated item |
| 10 | 13 | Textiles | Water repellency | CNS 10461 | Spray test device | Once every three years | 2013 | TESTEX |
| 11 | 14 | Textiles | Dryness | CNS 12915 | Drying time measuring device | Once per year | 2012 2013 2014 | Not designated item |
| 12 | 15 | Textiles | Mass | CNS 12915 sec 6.4 | Balance | Once every three years | 2013 | TESTEX、AATCC |
| 13 | 16 | Packaged Drinking Water | Heavy metal | NIEA W311.51B | ICP-AES | Once per year | 2012 2013 2014 | FAPAS |
| 14 | 17 | Jam | Preservative | CNS 10949 | GC-FID | Once every two years | 2012 2014 | P006 |
| 15 | 18 | Vegetables, fruits | Pesticide Residues | TFDA No. 0991900925 | LC/MS/MS | Once per year | 2012 2013 2014 | AOAC |
| 16 | 19 | Apple Juice | pH | CNS 6492 | pH meter | Once per year | 2013 | Not designated item |
| 16 | 20 | Apple Juice | acidity | CNS 8626 | pH meter & Titrator | Once per year | 2012 2014 | Not designated item |
| 17 | 21 | Apple Juice | Sugar content | CNS 12569 | Abbe Refractometer | Once per year | 2012 2013 2014 | Not designated item |
| 18 | 22 | Pork meat | Residue of Veterinary Drugs - tetracycline | TFDA No. 0939300627 | LC/MS/MS | Once per year | 2012 | FAPAS |
| 18 | 23 | Aquatic product | Residue of Veterinary Drugs -Nitrofuran Metabolites | TFDA No. 0991900821 | LC/MS/MS | Once per year | 2013 | FAPAS |
| 18 | 24 | Shrimp | Residue of Veterinary Drugs -Malachite Green and its Metabolite | TFDA No. 0971800008 | LC/MS/MS | Once per year | 2014 | FAPAS |
| 19 | 3 | Aluminum alloy | Elemental analysis | ASTM E1251 | SPARK-OES | Once every two years | 2012 2014 | CTS |

3.7	Review the PT plan regularly and revise timely

The laboratory may conduct a review (usually conducted together with the management review meeting) based on the PDCA principles, changes in the scope of accreditation, changes in regulatory requirements, changes in the level of risk factor (such as, staff turnover, changes in measurement techniques, acquisition of reference materials, etc.). Where circumstances require, plan shall be modified to suit requirements.

4.	Conclusion

Referring to the foregoing case study, a laboratory staff familiar with the testing techniques and laboratory operation could very easily conduct a risk assessment of the related factors based on the level of significance of their effects on the measurement results, and then follow the proficiency testing participation requirements of the accreditation organization to establish a PT plan suited to the particular requirements of the laboratory.

Under the same principle, the accreditation organization may employ risk assessment concepts to define the minimum requirements for the proficiency testing participation item and frequency of the accredited laboratory. For instance, the TAF, pursuant to the accreditation risk assessment, define that the frequency shall be set at once a year for items which involve food product for direct oral ingestion that may immediately affect the human body (such as, pesticide residues of produce, veterinary medicine residue of livestock, heavy metals, etc.). If items involves product that is taken through skin contact or oral ingestion, and would require long period of accumulation before it may affect the human body, the frequency shall be set at once in two years. When no evidence of direct effects on human health is determined, participating once within a period of three years shall be required. This way, the accreditation organization may maintain a grasp of the conditions under which a laboratory maintains its technical competence and the laboratory need not waste its resources in participating in unnecessary proficiency testing programs !

References

1. TAF-CNLA-R05(4) Requirements for Proficiency Testing Activity, Taiwan Accreditation Foundation, May 2012.

2. Guidance on the level and frequency of proficiency testing participation, EA-4/18:2010.

# Text boxes

Identify all of the sub-disciplines and assess amount of participation

Identify the level of risk of the sub-discipline and determine frequency of participation

Search for a proficiency testing provider possessing the required competence

Establish an official PT plan

Regularly review the PT plan and its results